## Slide 1: täkō: A Polymorphic Cache Hierarchy for General-Purpose Optimization of Data Movement
Brian C. Schwedock, Piratach Yoovidhya, Jennifer Seibert, Nathan Beckmann
ISCA 2022
Session 1: Best Paper Nominees

## Slide 2: Data movement costs keep getting worse
50 years
Loads & stores
Core
Memory
LLC slice
Core & L1
L2
Memory
Memory
1000x

## Slide 3: Specialized memory hierarchies give big gains!
Graph optimizations
Data placement
System software (e.g., file system)
Sparse linear algebra / machine learning
Approximation / compression
Data marshalling / layout
Pointer chasing
Memoization
Prefetching
Relaxed coherence / consistency
Memory management
…
- Big opportunity -
Often >2x end-to-end speedup!
LLC slice
Core & L1
L2
Memory
Memory
Specialized hardware  Not going to happen!!!

## Slide 4: How can we specialize the memory hierarchy without specialized hardware?

## Slide 5: The interface is the problem!
Current systems
täkō
Loads & stores
Core
Memory
Specialized hierarchies
Shared Cache
Memory
Private Cache
Core
Shared Cache
Memory
Private Cache
Core
Shared Cache
Memory
Private Cache
Core
ASICs
Software-controlled
Hardware-controlled
Software’s view
Engine

## Slide 6: täkō: A Polymorphic Cache Hierarchy for General-Purpose Optimization of Data Movement
Memory
Memory

## Slide 7: täkō: A Polymorphic Cache Hierarchy for General-Purpose Optimization of Data Movement
Memory
Memory
täkō makes memory-hierarchy specialization practical

## Slide 8: täkō exposes data movement to software
Cache
Memory
Core
Phantom Data
täkō Engine
Normal Data
Miss
Data
Load
Load
App Code
onMiss()
onEviction()
onWriteback()
App Code
Solution: Tell software when data moves! (& let it do something)
Baseline loads &
stores work normally
“Phantom” data lives
only in caches! [Carter, HPCA’99]
Software serves
misses to phantom
data (& evictions)

## Slide 9: Prior near-data computing is insufficient
Cache
Memory
Core
Engine
Data
App Code
Engines triggered by cores
Prior NDC
Cache
Memory
Core
Engine
App Code
Data
Engines triggered by data movement
täkō
täkō inspired by programmable memory hierarchies from the ‘90s
But enables new memory semantics, vs. optimizing loads & stores
[Kuskin, ISCA’94] [Reinhardt, ISCA’94] [Agarwal, ISCA’95] [Horowitz, ISCA‘96] [Carter, HPCA’99] [Shacham, DAC’09]

## Slide 10: Outline
Introduction
Motivation
Design
Evaluation

## Slide 11: Motivating Example: Lossy Compression

## Slide 12: Base+delta (B+Δ) lossy compression
Base
Δ
Δ
Δ
Δ
+
+
+
+
Compressed
Decompressed
Base
Δ
Δ
…
≈
≈
≈
≈
…

## Slide 13: B+Δ decompression: in the core
Private Cache
Core
Shared Cache
Memory
B
Δ
Pros: Reduced memory and cache usage
Cons: Decompress on every access
B
Δ
+
≈
Load
B
Δ
B
Δ
B
Δ

## Slide 14: B+Δ decompression: compressed caches?
B
Δ
Private Cache
Core
Shared Cache
Memory
Pros:
Reduced memory and cache usage
Reuse decomp. data in private cache
Cons:
Compression scheme fixed in hardware
Cannot support lossy compression
B
Δ
+
≈
Load
B
Δ
B
Δ
[Miguel, MICRO’15]

## Slide 15: B+Δ decompression: täkō
Load
phantom
Core
Private Cache
Shared Cache
Memory
B
Δ
Pros:
Reduced memory and cache usage
Reuse decomp. data in private cache
SW can implement any compression scheme!
… without needing new hardware for each!
✅
onMiss()
täkō Engine
B
Δ
+
≈
B
Δ

## Slide 16: Evaluation: täkō leverages cache to capture reuse
16K objects, 32K accesses, Zipfian distribution (full experimental methodology shown later)
Decompress on each access
Offload each decompression to L2
Data-movement triggers decompression on cache miss!
täkō with an ideal engine

## Slide 17: The interface is the problem
täkō
Loads & stores
Core
Memory
Shared Cache
Memory
Private Cache
Core
Software-controlled
Hardware-controlled
täkō is the solution
Engine
Software’s view

## Slide 18: täkō Design: Programming Interface

## Slide 19: täkō programming interface
Callback
Description
onMiss(void* addr)
Generate & fill in cache line at addr.
onEviction(void* addr)
Handle eviction of clean data.
onWriteback(void* addr)
Handle eviction of dirty data.

## Slide 20: Registering callbacks
Address range
onMiss()
onEviction()
onWriteback()
MorphA
register(MorphA, L2, 4 MB)
register(MorphA, LLC, 8 MB)
register(MorphB, L2, 6 MB)
MorphB
onMiss()
onEviction()
onWriteback()
0x0000
0xFFFF
Normal data

## Slide 21: täkō Design: Architecture

## Slide 22: täkō architecture
Callback Buffer
Dataflow Fabric
L1d
rTLB
TLB
Hardware Scheduler
Tile
Core
Data Array
Tag Array
L2
Engine
L1d
L1i
L3 Cache Bank

## Slide 23: onMiss callback
Callback Buffer
L1d
rTLB
TLB
Hardware Scheduler
Core
Data Array
Tags
L2
Engine
L1d
L1i
L3 Cache Bank
GET A
L3 miss
Scheduled
onMiss(A)
Response
L1 hit
1
2
3
4
6
∞
Fill A
5

## Slide 24: onWriteback callback
Callback Buffer
L1d
rTLB
TLB
Hardware Scheduler
Core
Data Array
Tags
L2
Engine
L1d
L1i
L3 Cache Bank
A evicted
(✔ = registered)
1
onWriteback(A)
A ✔
Invalidate A
2
4
Scheduled
3

## Slide 25: Additional cache and engine state
Dataflow Fabric
Data Array
L2
L3 Cache Bank
Engine
Core
L1d
L1i
TLB
Hardware Scheduler
Callback Buffer
Tag Array
L1d
rTLB
TLB
2 bits per TLB entry
1 bit per tag
Callback buffer
Engine L1d
Engine TLB
Engine reverse TLB
< 3% overhead vs. L3 cache

## Slide 26: Engine microarchitecture
Engine Dataflow Fabric
Engine L1d
≈3% state overhead (vs L3 cache)
Processing Element
ALUs
Fabric Network
Token store
Fabric Network
Instr memory
Similar to triggered instructions
[Parashar, ISCA’13]
op1
op2
pred
tid
op
imm
etc

## Slide 27: Why dataflow?
Callbacks need memory-level parallelism
Callbacks are typically short
Callbacks are executed repeatedly
Multiple callbacks execute in parallel
Engine Dataflow Fabric
Engine L1d

## Slide 28: Evaluation: Case Studies

## Slide 29: Evaluation methodology
Cycle-level simulation of 16-tile CMP
Tile contains: OoO main core and täkō engine
täkō dataflow fabric: 5x5 array, 1-cycle PE latency
Ideal fabric: infinite PEs, 0-cycle PE latency
Dataflow Fabric
rTLB
Core
Data Array
Tag Array
L2
L3 Cache Bank
L1d
L1i
Engine
L1d
TLB
TLB
Callback Buffer
Hardware Scheduler

## Slide 30: Case studies
  In-cache data transformation
  Commutative scatter-updates
  Decoupled graph traversals
  Transactions on NVM
  Detect cache side-channel attacks

## Slide 31: Case Study: Commutative Scatter-updates

## Slide 32: Commutative scatter-updates in graphs
Scatter-updates are common in graph algorithms:
But current cache hierarchies are bad at scatter-updates
  Conflict between pull vs. push semantics
   Excess bandwidth & synchronization
for src in vertices:
for dst in outNeighbors(src):
vertex(dst) += vertex(src)
1
0
2
4
3
PHI: Architectural Support for Synchronization- and Bandwidth-Efficient Commutative Scatter Updates. [Mukkara+, MICRO’19]

## Slide 33: Commutative scatter-updates in graphs
PHI changes the memory hierarchy to have push-based semantics
1. Updates are buffered in-cache without accessing memory
2. Updates applied on eviction:
  2a) Immediately in-place, or
  2b) Logged & deferred [Beamer, IPDPS’17]
Updates moved off critical path
Bandwidth optimized by 2a) vs 2b)
PHI: Architectural Support for Synchronization- and Bandwidth-Efficient Commutative Scatter Updates. [Mukkara+, MICRO’19]
UPDATE 0xFOO, +4
Cache
Core
Memory
4
UPDATE 0xFOO, +2
6
0xFOO
0xFOO
10
2a) +6 in-place
16
0xFOO: +6
2b) Log & defer

## Slide 34: Example: PHI on täkō
Memory
B
F
E
A
Core
L3
L2
Engine
Bins
{F,1}
{B,0}
{E,2}
{C,3} {D,1}
Update Vertex
1
onWriteback can a) update in-place b) log update
onMiss zeroes lines
2
3b
3a
{B,1}
C
D
{B,1} {E,2}
{F,1}
Impossible in software without täkō’s callbacks!
Morph registered at L3 cache
Vertex updates buffered in phantom data
onWriteback selectively applies updates in-place or logs updates

## Slide 35: täkō’s benefits implementing PHI
PageRank, 16 threads, graph: 16M vertices & 160M edges
In-place
Log
In-place
Log
In-place
Log
Push-based PageRank
Software update-batching (always log)
täkō implementation of PHI
täkō with an ideal engine
[Beamer, IPDPS’17]

## Slide 36: Case Study: Detecting Side-channel Attacks

## Slide 37: Prime + probe cache attack
Shared LLC
Core
Core
Target set
1a. Attacker primes
target set
1b. Sensitive data
is evicted
2. Victim evicts
attacker data
3. Attacker probes
target set
Long-latency load
 attack successful!
 onEviction interrupts core before any info leaks!!

## Slide 38: Prime + probe: cache eviction trace
Target set
Without täkō
With täkō
✘
✅

## Slide 39: See the paper for full results
  In-cache data transformation: 2.2x speedup, 61% energy savings
  Commutative scatter-updates: 4.2x speedup, 36% energy savings
  Decoupled graph traversals: 43% speedup, 17% energy savings
  Transactions on NVM: 2.1x speedup, 47% energy savings
  Detect cache side-channel attacks
  Insensitive to system configuration and data sizes

## Slide 40: täkō: polymorphic cache hierarchy
The memory interface limits software capabilities
Specialized hierarchies are beneficial but impractical
täkō provides a general-purpose architecture to enable software optimization of the cache hierarchy
Dataflow Fabric
rTLB
Core
Data Array
Tag Array
L2
L3 Cache Bank
L1d
L1i
Engine
L1d
TLB
TLB
Callback Buffer
Hardware Scheduler